## Slide 1: Smart Home System

## Slide 2: Group members
Suhas S 20ETCS002137
Vishnu M V 20ETCS002154
Danesh S D 20ETCS002041
Badri Narayan 20ETCS002032
Rohit Kumar 20ETCS002108

## Slide 3: Technologies in Smart Home System
Smoke Detection and Extinction
Fire Detection and Alarm System
Temperature and Humidity Monitoring
IoT with Blynk Server

## Slide 4: Smoke Detection and Extinction
MQ-2 Smoke Detector
NodeMCU
BC547 NPN Transistor
1K Resistor
Exhaust Fan
Components Required

## Slide 5: Smoke Detection and Extinction
Connection Diagram
MQ2 | NodeMCU
VCC | Vin / 5V
GND | GND
A0 | A0
Transistor | 
Emitter | GND
Base | D6
 | Exhaust Fan
5V | Red
Collector | Black

## Slide 6: Fire Detection and Alarm System
NodeMCU
BC547 NPN Transistor
1K Resistor
Exhaust Fan
Components Required
IR Flame Sensor
Buzzer

## Slide 7: Fire Detection and Alarm System
Connection Diagram
Flame | NodeMCU
VCC | Vin / 5V
GND | GND
D0 | D5
Buzzer | 
Red | D5
Black | GND
Transistor | 
Emitter | GND
Base | D6
 | Exhaust Fan
5V | Red
Collector | Black

## Slide 8: Temperature and Humidity Monitoring
NodeMCU
BC547 NPN Transistor
1K Resistor
Exhaust Fan
Components Required
Buzzer
DHT11 Sensor

## Slide 9: Temperature and Humidity Monitoring
DHT 11 | NodeMCU
VCC | Vin / 5V
GND | GND
Data | D4
Buzzer | 
Red | D5
Black | GND
Transistor | 
Emitter | GND
Base | D6
 | Exhaust Fan
5V | Red
Collector | Black

## Slide 10
IoT with Blynk Server
Blynk is designed for the Internet of Things. It can control hardware remotely, it can display sensor data, it can store data, and can visualize it.
Blynk App - allows to you create amazing interfaces for your projects using various widgets we provide.
Blynk Server - responsible for all the communications between the smartphone and hardware.
Blynk Libraries - for all the popular hardware platforms - enable communication with the server and process all the incoming and outcoming commands.

## Slide 11: FlowChart
Start
MQ2
Flame
DHT11
?
Temp
?
Flame
?
Smoke
Fan
Alerts
END
Send DATA to Server
No
No
Yes
Yes
Yes
No
No

## Slide 12: Smart Home System

## Slide 13: Thank you